## Slide 1: MicroPython IoT Hackathon
Featuring the ESP8266
Jeff Fischer
Data-Ken Research
jeff@data-ken.org
https://data-ken.org
Sunnyvale, California, USA
April 2017

## Slide 2: Tonight’s Agenda
Overview lecture
Build and test system (hardware and software)
Additional projects (if time permits)

## Slide 3: Why Python for IoT?
High-level, easy to prototype ideas and explore options
Runs on embedded devices
Python data analysis ecosystem
Array and matrix processing
High level data analysis tools
Numerical analysis routines
HMMLearn
Machine learning

## Slide 4: Basic Electronics
Power
Supply
Circuit
+ (Vcc)
- (GND)
Current
Electrons
Voltage = Electrical Pressure
Current = Flow of electric charge
Resistance = Difficulty to pass
electric charge
Ohm’s Law
V = I R
resistance
current
voltage

## Slide 5: Digital Logic
Voltage
Vcc (5V or 3.3V)
GND (0V)
High (“1”)
Low (“0”)
Noise Margin

## Slide 6: Cautions
Do not connect power and ground directly to each other (“shorting”)
Chips are sensitive to static discharge, be careful
  You might touch some metal (e.g. your laptop chassis before handling the electronics)

## Slide 7: System Overview
ESP8266 breakout board
TSL2591 Lux Sensor
breakout board
I2C Bus
PC/Laptop
Terminal
session
MQTT
Broker
WiFi Access Point
and Router
USB Cable
MQTT over WiFi

## Slide 8: Steps
Hardware Assembly
Firmware and software install
Application to read the sensor
Messaging with MQTT

## Slide 9: Parts
Breadboard
Wires
USB Cable
Battery
TSL2591
Breakout
ESP8266
Breakout

## Slide 10: Recommended Tools
Multimeter
Soldering Iron
Wire Strippers
Wire Cutters
Solder
Needle-nose
Pliers

## Slide 11: Breadboards
30
29
2
1
. . .
Photo
Electrical Connections
Use for GND
Board
Use for Power
Use for pin connections
a
b
c
d
e
f
g
h
i
j

## Slide 12: System with Adafruit Feather HUZZAH
TSL2591
lux sensor
breakout
board
Lithium Ion
Polymer
Battery
3.7v 350mAh
MicroUSB to
USB cable
½ Size breadboard
Adafruit Feather HUZZAH
ESP8266 breakout board
Notes: 8266:
32-bit RISC CPU: Tensilica Xtensa LX106 running at 80 MHz
64 KiB of instruction RAM, 96 KiB of data RAM
Power: 15 mA if modem off, 50 – 170 mA when transmitting (http://bbs.espressif.com/viewtopic.php?t=133)

## Slide 13: Feather HUZZAH: Wiring Diagram
SDA
SCL
GND Bus
3V Bus
A3
A4
A1
A2
A5
A6

## Slide 14: System with NodeMCU
TSL2591
lux sensor
breakout
board
MicroUSB to
USB cable
NodeMCU
ESP8266
breakout board

## Slide 15: NodeMCU: Wiring Diagram
3V Bus
GND Bus
N1
N2
N3
N4
SDA
SCL
N5
N6

## Slide 16: Reading the Light Sensor
From thingflow import *
from tsl2591 import Tsl2591
tsl = Tsl2591('lux-1')
sched = Scheduler()
sched.schedule_sensor(tsl, 2.0, Output())
sched.run_forever()
Lux
Sensor
Output
Scheduler
Invokes once every 2 seconds

## Slide 17: MQTT
Broker
Topic1
Topic2
. . .
Client-A
Client-B
Client-C
Client-D
Client-F
Topic3
Publish
Publish
Publish
Subscribe
Publish
Subscribe
Subscribe
Client-E
Subscribe

## Slide 18: Client.py: Send events to MQTT
Lux
Sensor
MQTT
Writer
Scheduler
Invokes once every SLEEP_TIME seconds

## Slide 19: Client.py: Send events to MQTT
# Configuration is stored in a separate config.py
from config import SENSOR_ID, WIFI_ESSID, WIFI_PASSWORD, MQTT_HOST,\
MQTT_TOPIC, SLEEP_TIME
from wifi import wifi_connect, disable_wifi_ap
from thingflow import *
from tsl2591 import Tsl2591
from mqtt_writer import MQTTWriter
# setup network
disable_wifi_ap()
wifi_connect(WIFI_ESSID, WIFI_PASSWORD)
# create objects
m = MQTTWriter(SENSOR_ID, MQTT_HOST, 1883, MQTT_TOPIC)
tsl = Tsl2591(SENSOR_ID)
sched = Scheduler()
# schedule and run
sched.schedule_sensor(tsl, SLEEP_TIME, m)
print("Running main loop with sample every %s seconds..." % SLEEP_TIME)
sched.run_forever()

## Slide 20: Server.py
MQTT
Adapter
Map
to
UTF8
Parse
JSON
Overwrite
timestamp
Write to
CSV
file
mqtt.select(lambda m:(m.payload).decode('utf-8'))\
.from_json(constructor=SensorEvent)\
.select(lambda evt: SensorEvent(sensor_id=evt.sensor_id,
ts=time.time(),
val=evt.val))\
.csv_writer(filename)

## Slide 21: Today’s MQTT Setup
ESP8266 breakout board
TSL2591 Lux Sensor
breakout board
I2C Bus
Participant
Laptop
MicroPython
REPL
WiFi Access Point
and Router
USB Cable
MQTT over WiFi
MQTT
Broker
Raspberry Pi
Instructor
Laptop
mosquitto_sub
SSH login to Pi

## Slide 22: Next Steps
Follow the detailed instructions in the online documentation, starting with “Hardware Assembly”
You can skip the section on the MQTT broker – you can connect to my Raspberry Pi
If you get done early, take a look at the extra projects section. Some projects you might try:
  Graph the light data in Jupyter
  Turn on an LED
  Read a temperature sensor
  Read a door open/close sensor
Feel free to ask for help!

## Slide 23: Thank You
Questions?
More information
Email: jeff@data-ken.org
Hackathon Tutorial: http://micropython-iot-hackathon.readthedocs.io/en/latest/
Website and blog: https://data-ken.org
ThingFlow: https://github.com/mpi-sws-rse/thingflow-python