## Slide 1: MicroPython IoT Hackathon
Featuring the ESP8266
Jeff Fischer
Data-Ken Research
jeff@data-ken.org
https://data-ken.org
Sunnyvale, California, USA
January 2017

## Slide 2: Tonight’s Agenda
Overview lecture
Build and test system (hardware and software)
Additional projects (if time permits)

## Slide 3: Why Python for IoT?
High-level, easy to prototype ideas and explore options
Runs on embedded devices
Python data analysis ecosystem
Array and matrix processing
High level data analysis tools
Numerical analysis routines
HMMLearn
Machine learning

## Slide 4: Basic Electronics
Power
Supply
Circuit
+ (Vcc)
- (GND)
Current
Electrons
Voltage = Electrical Pressure
Current = Flow of electric charge
Resistance = Difficulty to pass
electric charge
Ohm’s Law
V = I R
resistance
current
voltage

## Slide 5: Digital Logic
Voltage
Vcc (5V or 3.3V)
GND (0V)
High (“1”)
Low (“0”)
Noise Margin

## Slide 6: System Overview
ESP8266 breakout board
TSL2591 Lux Sensor
breakout board
I2C Bus
PC/Laptop
Terminal
session
MQTT
Broker
WiFi Access Point
and Router
USB Cable
MQTT over WiFi

## Slide 7: Steps
Hardware Assembly
Firmware and software install
Application to read the sensor
Messaging with MQTT

## Slide 8: Parts
Breadboard
Wires
USB Cable
Battery
TSL2591
Breakout
ESP8266
Breakout

## Slide 9: Recommended Tools
Multimeter
Soldering Iron
Wire Strippers
Wire Cutters
Solder
Needle-nose
Pliers

## Slide 10: Breadboards
30
29
2
1
. . .
Photo
Electrical Connections
Use for GND
Board
Use for Power
Use for pin connections
a
b
c
d
e
f
g
h
i
j

## Slide 11: System with Adafruit Feather HUZZAH
TSL2591
lux sensor
breakout
board
Lithium Ion
Polymer
Battery
3.7v 350mAh
MicroUSB to
USB cable
½ Size breadboard
Adafruit Feather HUZZAH
ESP8266 breakout board
Notes: 8266:
32-bit RISC CPU: Tensilica Xtensa LX106 running at 80 MHz
64 KiB of instruction RAM, 96 KiB of data RAM
Power: 15 mA if modem off, 50 – 170 mA when transmitting (http://bbs.espressif.com/viewtopic.php?t=133)

## Slide 12: Feather HUZZAH: Wiring Diagram
SDA
SCL
GND Bus
3V Bus
A3
A4
A1
A2
A5
A6

## Slide 13: System with NodeMCU
TSL2591
lux sensor
breakout
board
MicroUSB to
USB cable
NodeMCU
ESP8266
breakout board

## Slide 14: NodeMCU: Wiring Diagram
3V Bus
GND Bus
N1
N2
N3
N4
SDA
SCL
N5
N6

## Slide 15: MQTT
Broker
Topic1
Topic2
. . .
Client-A
Client-B
Client-C
Client-D
Client-F
Topic3
Publish
Publish
Publish
Subscribe
Publish
Subscribe
Subscribe
Client-E
Subscribe

## Slide 16: Server.py
MQTT
Adapter
Map
to
UTF8
Parse
JSON
Overwrite
timestamp
Write to
CSV
file
mqtt.select(lambda m:(m.payload).decode('utf-8'))\
.from_json(constructor=SensorEvent)\
.select(lambda evt: SensorEvent(sensor_id=evt.sensor_id,
ts=time.time(),
val=evt.val))\
.csv_writer(filename)

## Slide 17: Thank You
Questions?
More information
Email: jeff@data-ken.org
Hackathon Tutorial: https://readthedocs.org/search/?q=micropython-iot-hackathon
Website and blog: https://data-ken.org
AntEvents: https://github.com/mpi-sws-rse/antevents-python